## Slide 1: Embedded Systems
1 - Introduction

## Slide 2: Organization
WWW:
Lecture:
https://lms.etao.net
Chen Bo, cb@zjut.edu.cn
References:
Edward A. Lee and Sanjit A. Seshia: Introduction to Embedded Systems, A Cyber- Physical Systems Approach, Second Edition, MIT Press, ISBN 978-0-262-53381-2, 2017.
M. Wolf: Computers as Components – Principles of Embedded System Design. Morgan Kaufman Publishers, ISBN 978-0-128-05387-4, 2016.
P. Marwedel: Embedded System Design, Springer, ISBN 978-3-319-56045-8, 2018.
G.C. Buttazzo: Hard Real-Time Computing Systems. Springer Verlag, ISBN 978-1-4614- 0676-1, 2011.
Sources:

## Slide 3: What will you learn?
Theoretical foundations and principles of the analysis and design of embedded systems.
Practical aspects of embedded system design, mainly software design.
The course has three components:
Lecture: Communicate principles and practical aspects of embedded systems.
Exercise: Use paper and pencil to deepen your understanding of analysis and
design principles .
Laboratory (ES-Lab): Introduction into practical aspects of embedded systems design. Use of state-of-the-art hardware and design tools.

## Slide 4: Embedded Systems - Impact

## Slide 5: Embedded Systems
Often, the main reason for buying is not information processing
Embedded systems (ES) = information processing systems embedded into a larger product
Examples:

## Slide 6
© www.braingrid.org
© www.openpr.com

## Slide 7: Many Names – Similar Meanings
© Edward Lee

## Slide 8: Embedded Systems are an essential component
Manyika, James, et al. Disruptive technologies: Advances that will transform life, business, and the global economy. Vol. 180. San Francisco, CA: McKinsey Global Institute, 2013.
麦肯锡：12项决定未来经济的颠覆性技术
…

## Slide 9: Embedded System
CYBER WORLD
PHYSICAL
WORLD
Nature
Hardware &
Software
Communication
observing influencing physical/biological/social
processes
Embedded System
Computation
reasoning deciding big data
使用反馈,通过在信息世界中做出明智的决定来影响物理世界的动态

## Slide 10: Predictability & Dependability
CPS = cyber-physical system
“It is essential to predict how a CPS is going to behave under any circumstances […] before it is deployed.”Maj14
“CPS must operate dependably, safely, securely, efficiently and in real-time.”Raj10
Maj14 R. Majumdar & B. Brandenburg (2014). Foundations of Cyber-Physical Systems.
Raj10 R. Rajkumar et al. (2010). Cyber-Physical Systems: The Next Computing Revolution.

## Slide 11: Efficiency & Specialization
Embedded systems must be efficient:
  Energy efficient
  Code-size and data memory efficient
  Run-time efficient
  Weight efficient
  Cost efficient
Embedded Systems are often specialized towards a certain application or application domain:
Knowledge about the expected behavior and the system environment at design time is exploited to minimize resource usage and to maximize predictability and reliability.利用有关在设计时的预期行为和系统环境的知识，以最大程度地减少资源使用并最大程度地提高可预测性和可靠性。

## Slide 12: Reactivity & Timing
Embedded systems are often reactive:
Reactive systems must react to stimuli from the system environment :
„A reactive system is one which is in continual interaction with is environment and executes at a pace determined by that environment“ [Bergé, 1995]
Embedded systems often must meet real-time constraints:
For hard real-time systems, right answers arriving too late are wrong. All other time-constraints are called soft. A guaranteed system response has to be explained without statistical arguments.
„A real-time constraint is called hard, if not meeting that constraint could result in a catastrophe“ [Kopetz, 1997].

## Slide 13: Comparison
Embedded Systems:
Few applications that are known at
design-time.
Not programmable by end user.
Fixed run-time requirements (additional
computing power often not useful).
Typical criteria:
  cost
  power consumption
  size and weight
  dependability
  worst-case speed
General Purpose Computing
Broad class of applications.
Programmable by end user.
Faster is better.
Typical criteria:
  cost
  power consumption
  average speed

## Slide 14: Lecture Overview
Introduction to Embedded Systems
Software Development
Hardware-Software Interface
Programming Paradigms
Embedded Operating Systems
Real-time Scheduling
Shared Resources
Hardware Components
Power and Energy
Architecture Synthesis
Software
Hardware
Hardware-
Software

## Slide 15: Components and Requirements by Example

## Slide 16
Bitcraze.io

## Slide 17: Components and Requirements by Example - Hardware System Architecture -

## Slide 18: High-Level Block Diagram View

## Slide 20: High-Level Physical View

## Slide 21: High-Level Physical View

## Slide 22: Low-Level Schematic Diagram View
(1 page out of 3)
LEDs

## Slide 23: Low-Level Schematic Diagram View
(1 page out of 3)
Motors

## Slide 24: High-Level Software View
The software is built on top of a real-time operating system “FreeRTOS”.
We will use the same operating system in the ES-Lab … .

## Slide 25: High-Level Software View
The software architecture supports
real-time tasks for motor control (gathering sensor values and pilot commands, sensor fusion, automatic control, driving motors using PWM (pulse width modulation, … ) but also
non-real-time tasks (maintenance and test, handling external events, pilot
commands, … ).
Control System:
PID controller (proportional–integral–derivative)
sensors
motors
pilot commands
(from wireless interface)
update frequencies (periodic task execution)

## Slide 26: High-Level Software View
The software architecture supports
real-time tasks for motor control (gathering sensor values and pilot commands, sensor fusion, automatic control, driving motors using PWM (pulse width modulation, … ) but also
non-real-time tasks (maintenance and test, handling external events, pilot
commands, … ).

## Slide 27: High-Level Software View
1 - 40
Block diagram of the stabilization system:
sensor reading & analog-digital conversion
on sensor
component
transfer to processor
cleaning and preprocessing
automatic control
information extraction from sensors
actuation

## Slide 28: Components and Requirements by Example - Processing Elements -

## Slide 29: What can you do to increase performance?

## Slide 30: From Computer Engineering 1
2015
Intel 62-Core Xeon Phi

## Slide 31: From Computer Engineering 1:
AMD multicore RYZEN

## Slide 32: From Computer Engineering 1
Intel Xeon Phi 7290 (8 Billion transistors, 14nm technology,
~ 650mm2 area,
1.5 GHZ clock frequency)

## Slide 33: What can you do to decrease power consumption?

## Slide 34: Embedded Multicore Example
Recent developments:
Specialize multicore processors towards real-time processing and low power
consumption
Target domains:

## Slide 35: Why does higher parallelism help in reducing power?

## Slide 36: System-on-Chip
Samsung Galaxy S6
Exynos 7420 System on a Chip (SoC)
8 ARM Cortex processing cores (4 x A57, 4 x A53)
30 nanometer: transistor gate width
Exynos 5422

## Slide 37: How to manage extreme workload variability?

## Slide 38: ARM big.LITTLE Architecture

## Slide 39: Components and Requirements by Example - Systems -

## Slide 40: Zero Power Systems and Sensors
Streaming information to and from the physical world:
“Smart Dust”
Sensor Networks
Cyber-Physical Systems
Internet-of-Things (IoT)

## Slide 41: Zero Power Systems and Sensors 零功耗系统与传感器
IEEE Journal of Solid-State Circuits, April 2017, 961-971.
IEEE Journal of Solid-State Circuits, Jan 2013, 229-243.

## Slide 42: Trends …
Embedded systems are communicating with each other, with servers or with the cloud.
Communication is increasingly wireless.
Higher degree of integration on a single chip or integrated components:
  Memory + processor + I/O-units + (wireless) communication.
  Use of networks-on-chip for communication between units.
  Use of homogeneous or heterogeneous multiprocessor systems on a chip (MPSoC).
  Use of integrated microsystems that contain energy harvesting, energy storage, sensing, processing and communication (“zero power systems”).
  The complexity and amount of software is increasing.
Low power and energy constraints (portable or unattended devices) are increasingly important, as well as temperature constraints (overheating).
There is increasing interest in energy harvesting to achieve long term autonomous operation.