## Slide 1: Embedded Programming with the GNU Toolchain
嵌入式开发 - GNU工具链

## Slide 2: What?
C Application
OS
Hardware
C Application
Hardware
Conventional C Programs
Our Case

## Slide 3: Why?
●
Embedded Firmware Development RTOS development – eCOS, RTEMS, ... Bootloader development – U-Boot, ...
Programming DSPs
Testing Microprocessors cores implemented in ASICs / FPGAs
●
●
●
●

## Slide 4: How?
●
3 Example Scenarios
Hello Embedded World – Add 2 numbers in registers in assembly
Add 2 numbers from memory in assembly Add 2 numbers from memory in C
●
●
●

## Slide 5: Scenario I - Overview
●
Cortex-M3 Processor Writing Assembly Programs
Emulating Cortex-M3 with Qemu
●
●

## Slide 6: ARMv7
●
Latest revision of ARM architecture – ARMv7
Cortex Processor – ARMv7 implementation
Profiles
A Profile – GPOS and applications
R Profile – optimized for realtime systems
M Profile – optimized for low cost embedded systems
●
●

## Slide 7: Cortex-M3 Features
●
Thumb-2 Instruction Set Bit Banding
Integrated Peripherals
NVIC
Memory Protection Unit (MPU)
Debug Peripherals
●
●

## Slide 8: CM3 SoCs
●
SoC vendors license CM3 from ARM SoC vendors use it as building block Licensees
TI – Stellaris processors
Atmel – ATSAM3U series
STMicroelectronics – STM32
NXP - LPC1700
●
●

## Slide 9: LM3S811
●
Cortex-M3 core Memory
64KB Flash
8KB RAM
Peripherals
10 bit ADCs
I2C, SPI, UARTs, PWM
32 GPIOs
●
●

## Slide 10: Registers
●
Load Store Architecture
Data processing instructions – register operands
Large register file – 16 32-bit registers
●
●

## Slide 11: Registers (Contd.)
R0
R1
R2
R3
R4
R5
R6
R7
R8
R9
R10
R11
R12
R13 (SP)
R14 (LR)
R15 (PC)
PSR
CONTROL
PRIMASK
FAULTMASK
BASEPRI
●
R0 – R12
General Purpose
R13
Stack Pointer
R14
Link Register
R15
Program Counter
●
●
●

## Slide 12: Memory Map
●
CM3 has a fixed memory map
Easy to port software
4GB Address Space LM3S811
64KB Flash
8KB SRAM
●
●
●
Peripherals
SRAM
Flash
0x0000_0000
0x2000_0000
0x4000_0000

## Slide 13: Reset
●
SP from address 0x0 PC from address 0x4
Address is mapped to Flash
●
●
Reset Vec.
Initial SP
0x0004
0x0000

## Slide 14: Assembly
●
label: convenient way to refer to the memory location
instruction: ARM instruction or assembler directive
comment: starts with @
●
●
label: instruction @comment

## Slide 15: Hello Embedded World
.thumb
.syntax unified
.word 0x100
.word start+1
sp: reset:
start: |  |  | 
 | mov | r0, | #5
 | mov | r1, | #4
 | add | r2, | r1, r0
stop: b stop

## Slide 16: Toolchain
Assembler (as)
Linker (ld)
Assembler Source (.s)
Object File (.o)
Executable (.elf)

## Slide 17: Toolchain (Contd.)
$ arm-none-eabi-as -mcpu=cortex-m3 -o add.o add.s
●
Cross toolchain prefix - arm-none-eabi-
-mcpu=cortex-m3 Specifies the CPU
-o Specifies the output file
●
●

## Slide 18: Toolchain (Contd.)
$ arm-none-eabi-ld -Ttext=0x0 -o add.elf add.o
●
Cross toolchain prefix - arm-none-eabi-
-Ttext=0x0 Addresses should be assigned to instructions starting from 0.
-o Specifies the output file
●
●

## Slide 19: Toolchain (Contd.)
$ arm-none-eabi-nm add.elf
... |  | 
00000004 | t | reset
00000000 | t | sp
00000008 | t | start
00000014 | t | stop
●
List symbols from object file
Verify initial SP and reset vector are located at required address
●

## Slide 20: Toolchain (Contd.)
●
ELF file format contains meta information for OS
Binary format contains consecutive bytes starting from an address
Convenient for flashing tools
●
●

## Slide 21: Toolchain (Contd.)
$ arm-none-eabi-objcopy -O binary add.elf add.bin
●
objcopy – converts between different executable file formats
-O specifies that output file format
●

## Slide 22: Qemu
●
Open source machine emulator - the processor and the peripherals
Architectures – i386, ARM, MIPS, SPARC ... Used by various open source projects
OLPC
OpenMoko
Linux Kernel Testing
Android emulator
●
●

## Slide 23: Emulating in Qemu
$ qemu-system-arm -M lm3s811evb -kernel add.bin
●
-M lm3s811evb specifies the machine to be emulated
-kernel specifies data to be loaded in Flash from address 0x0
monitor interface – control and status can be used to view the registers
●
●
●

## Slide 24: Review
●
Writing simple assembly programs
Building and linking them using GNU Toolchain
Emulating Cortex-M3 processor using Qemu
●
●

## Slide 25: Scenario II - Overview
●
Role of Linker Linker Scripts Placing data in RAM
●
●

## Slide 26: Linker
assembler
a.s
a.o
assembler
b.s
b.o
assembler
c.s
c.o
linker
abc.o
●
In multi-file programs – combines multiple object files to form executable

## Slide 27: Linker (Contd.)
Linker
Symbol Resolution
Relocation
Section Merging
Section Placement

## Slide 28: Linker (Contd.)
Linker
Symbol Resolution
Relocation
Section Merging
Section Placement

## Slide 29: Symbol Resolution
●
Functions are defined in one file
Referenced in another file
References are marked unresolved by the compiler
Linker patches the references
●
●
●

## Slide 30: Linker
Linker
Symbol Resolution
Relocation
Section Merging
Section Placement

## Slide 31: Relocation
●
Code generated assuming it starts from address X
Code should start from address Y
Change addresses assigned to labels
Patch label references
●
●
●

## Slide 32: Sections
●
Placing related bytes at a particular location.
Example:
instructions in Flash
data in RAM
Related bytes are grouped together using sections
Placement of sections can be specified
●
●
●

## Slide 33: Sections (Contd.)
●
Most programs have atleast two sections,
.text and .data
Data or instructions can be placed in a section using directives
Directives
.text
.data
.section
●
●

## Slide 34: Sections (Contd.)
●
Source – sections can be interleaved Bytes of a section – contiguous addresses
●

## Slide 35: Linker
Linker
Symbol Resolution
Relocation
Section Merging
Section Placement

## Slide 36: Section Merging
●
Linker merges sections in the input files into sections in the output file
Default merging – sections of same name
Symbols get new addresses, and references are patched
Section merging can be controlled by linker script files
●
●
●

## Slide 37: Linker
Linker
Symbol Resolution
Relocation
Section Merging
Section Placement

## Slide 38: Section Placement
●
Bytes in each section is given addresses starting from 0x0
Labels get addresses relative to the start of section
Linker places section at a particular address
Labels get new address, label references are patched
●
●
●

## Slide 40
strlen

## Slide 42: Linker Script
Linker
Symbol Resolution
Relocation
Section Merging
Section Placement
Can be controlled through Linker scripts.
42

## Slide 43: Simple Linker Script
43
MEMORY {
FLASH (rx) : ORIGIN = 0x00000000, LENGTH = 0x10000 SRAM (rwx) : ORIGIN = 0x20000000, LENGTH = 0x2000
}
SECTIONS {
.text : {
abc.o (.text);
def.o (.text);
} > FLASH
}
def.o (.text)
abc.o (.text)
0x0
0xFFFF

## Slide 44: Simple Linker Script
MEMORY {
FLASH (rx)
SRAM (rwx)
}
: | ORIGIN | = | 0x00000000, | LENGTH | = | 0x10000
: | ORIGIN | = | 0x20000000, | LENGTH | = | 0x2000
SECTIONS {
.text : {
abc.o (.text);
def.o (.text);
} > FLASH
}
Section Merging
44

## Slide 45: Simple Linker Script
: | ORIGIN | = | 0x00000000, | LENGTH | = | 0x10000
: | ORIGIN | = | 0x20000000, | LENGTH | = | 0x2000
MEMORY {
FLASH (rx)
SRAM (rwx)
}
SECTIONS {
.text : {
abc.o (.text);
def.o (.text);
} > FLASH
}
Section Placement
45

## Slide 46: Making it Generic
MEMORY {
FLASH (rx)
SRAM (rwx)
}
: | ORIGIN | = | 0x00000000, | LENGTH | = | 0x10000
: | ORIGIN | = | 0x20000000, | LENGTH | = | 0x2000
SECTIONS {
.text : {
* (.text);
} > FLASH
}
Wildcards to represent .text form all input files
46

## Slide 47: Multiple Sections
SECTIONS {
.text : {
* (.text);
} > FLASH
.rodata : {
* (.rodata);
} > FLASH
}
Dealing with mutiple sections
.rodata
.text
47
MEMORY {
FLASH (rx) : ORIGIN = 0x00000000, LENGTH = 0x10000 SRAM (rwx) : ORIGIN = 0x20000000, LENGTH = 0x2000
}
0xFFFF
0x0

## Slide 48: Data in RAM
48
●
Add two numbers from memory Assembly source
Linker Script
●
●

## Slide 49: RAM is Volatile!
49
●
RAM is volatile
Data cannot be made available in RAM at power-up
All code and data should be in Flash at power-up
Startup code – copies data from Flash to RAM
●
●
●

## Slide 50: RAM is Volatile! (Contd.)
50
●
.data section should be present in Flash at power-up
Section has two addresses
load address (aka LMA)
run-time address (aka VMA)
So far only run-time address – actual address assigned to labels
Load address defaults to run-time address
●
●
●

## Slide 51: Linker Script Revisited
.data
.text
MEMORY {
FLASH (rx) : ORIGIN = 0x00000000, LENGTH = 0x10000 SRAM (rwx) : ORIGIN = 0x20000000, LENGTH = 0x2000
}
SECTIONS {
.text : {
* (.text);
} > FLASH
.data : {
* (.data);
} > SRAM
}
0x00000000
0x0000FFFF
Flash
0x20000000
0x20001FFF
SRAM
51

## Slide 52: Linker Script Revisited
.data
.data
.text
MEMORY {
FLASH (rx) : ORIGIN = 0x00000000, LENGTH = 0x10000 SRAM (rwx) : ORIGIN = 0x20000000, LENGTH = 0x2000
}
SECTIONS {
.text : {
(.text);
} > FLASH
.data : {
(.data);
0x0000FFFF
Flash
0x20000000
0x20001FFF
SRAM
}
>
SRAM
AT>
FLASH
0x00000000
}
52

## Slide 53: Linker Script Revisited
.data
.data
.text
MEMORY {
FLASH (rx)
SRAM (rwx)
}
: | ORIGIN | = | 0x00000000, | LENGTH | = | 0x10000
: | ORIGIN | = | 0x20000000, | LENGTH | = | 0x2000
SECTIONS {
.text : {
* (.text);
etext = .;
} > FLASH
.data : {
sdata = .;
* (.data);
edata = .;
} > SRAM AT> FLASH
}
etext
53
edata sdata

## Slide 54: Data in RAM
54
●
Copy .data from Flash to RAM
start: ldr |  | r0, | =sdata |  | @ | Load | the | address | of | sdata
ldr |  | r1, | =edata |  | @ | Load | the | address | of | edata
ldr |  | r2, | =etext |  | @ | Load | the | address | of | etext
copy: | ldrb strb | r3, r3, | [r2] [r0] |  | @ @ | Load the value from Flash Store the value in RAM |  |  |  | 
add |  | r2, | r2, | #1 | @ | Increment |  | Flash pointer |  | 
add |  | r0, | r0, | #1 | @ | Increment |  | RAM pointer |  | 
cmp r0, r1 bne copy
@ Check if end of data
@ Branch if not end of data

## Slide 55: Review
55
●
Linker Script can control
Section Merging
Section Placement
.data placed in RAM, .text in Flash RAM is volatile
at load time .data is in Flash
at startup .data is copied from Flash to RAM
●
●
●
●

## Slide 56: Scenario III - Overview
56
●
C Environment Requirements C Sections
C Source Code Linker Script
●
●
●

## Slide 57: Doing it in C
●
Environment has to be setup
Stack pointer
Non-initalized global variables, initialized to zero
Initialized global variables must have their initial value
57

## Slide 58: C Sections
58
●
Sections created by GCC
.text – for functions
.data – for initialized global data
.bss – for uninitialized global data
.rodata – for strings and global variables defined as const

## Slide 59: Credits
59
●
Cash Register – Nikola Smolenski
Cerebral Cortex - www.toosmarttostart.samhsa.gov
Reset Button – flattop341 http://www.flickr.com/photos/flattop341/224175619/
Church Relocation – Fletcher6 http://commons.wikimedia.org/wiki/File:Salem_Church_Relocation.JP
Rope Image - Markus BÃ¤rlocher http://commons.wikimedia.org/wiki/File:Schotstek_links.jpg
●
●
●
●

## Slide 60: Further Reading
60
●
Embedded Programming using the GNU Toolchain - http://www.bravegnu.org/gnu-eprog/
GNU Linker Manual GNU Assembler Manual
●
●