## Slide 1: ARM instruction set
ARM versions.
ARM assembly language.
ARM programming model.
ARM memory organization.
ARM data operations.
ARM flow of control.

## Slide 2: ARM versions
ARM architecture has been extended over several versions.
We will concentrate on ARM7.

## Slide 3: ARM assembly language
Fairly standard assembly language:
LDR r0,[r8] ; a comment
label ADD r4,r0,r1

## Slide 4: ARM programming model
r0
r1
r2
r3
r4
r5
r6
r7
r8
r9
r10
r11
r12
r13
r14
r15 (PC)
CPSR
31
0
N Z C V

## Slide 5: Endianness
Relationship between bit and byte/word ordering defines endianness:
byte 3
byte 2
byte 1
byte 0
byte 0
byte 1
byte 2
byte 3
bit 31
bit 0
bit 0
bit 31
little-endian
big-endian

## Slide 6: ARM data types
Word is 32 bits long.
Word can be divided into four 8-bit bytes.
ARM addresses cam be 32 bits long.
Address refers to byte.
  Address 4 starts at byte 4.
Can be configured at power-up as either little- or bit-endian mode.

## Slide 7: ARM status bits
Every arithmetic, logical, or shifting operation sets CPSR bits:
  N (negative), Z (zero), C (carry), V (overflow).
Examples:
  -1 + 1 = 0: NZCV = 0110.
  231-1+1 = -231: NZCV = 1001.

## Slide 8: ARM data instructions
Basic format:
  ADD r0,r1,r2
  Computes r1+r2, stores in r0.
Immediate operand:
  ADD r0,r1,#2
  Computes r1+2, stores in r0.

## Slide 9: ARM data instructions
ADD, ADC : add (w. carry)
SUB, SBC : subtract (w. carry)
RSB, RSC : reverse subtract (w. carry)
MUL, MLA : multiply (and accumulate)
AND, ORR, EOR
BIC : bit clear
LSL, LSR : logical shift left/right
ASL, ASR : arithmetic shift left/right
ROR : rotate right
RRX : rotate right extended with C

## Slide 10: Data operation varieties
Logical shift:
  fills with zeroes.
Arithmetic shift:
  fills with ones.
RRX performs 33-bit rotate, including C bit from CPSR above sign bit.

## Slide 11: ARM comparison instructions
CMP : compare
CMN : negated compare
TST : bit-wise test
TEQ : bit-wise negated test
These instructions set only the NZCV bits of CPSR.

## Slide 12: ARM move instructions
MOV, MVN : move (negated)
MOV r0, r1 ; sets r0 to r1

## Slide 13: ARM load/store instructions
LDR, LDRH, LDRB : load (half-word, byte)
STR, STRH, STRB : store (half-word, byte)
Addressing modes:
  register indirect : LDR r0,[r1]
  with second register : LDR r0,[r1,-r2]
  with constant : LDR r0,[r1,#4]

## Slide 14: ARM ADR pseudo-op
Cannot refer to an address directly in an instruction.
Generate value by performing arithmetic on PC.
ADR pseudo-op generates instruction required to calculate address:
  ADR r1,FOO

## Slide 15: Example: C assignments
C:
  x = (a + b) - c;
Assembler:
ADR r4,a ; get address for a
LDR r0,[r4] ; get value of a
ADR r4,b ; get address for b, reusing r4
LDR r1,[r4] ; get value of b
ADD r3,r0,r1 ; compute a+b
ADR r4,c ; get address for c
LDR r2[r4] ; get value of c

## Slide 16: C assignment, cont’d.
SUB r3,r3,r2 ; complete computation of x
ADR r4,x ; get address for x
STR r3[r4] ; store value of x

## Slide 17: Example: C assignment
C:
  y = a*(b+c);
Assembler:
  ADR r4,b ; get address for b
  LDR r0,[r4] ; get value of b
  ADR r4,c ; get address for c
  LDR r1,[r4] ; get value of c
  ADD r2,r0,r1 ; compute partial result
  ADR r4,a ; get address for a
  LDR r0,[r4] ; get value of a

## Slide 18: C assignment, cont’d.
  MUL r2,r2,r0 ; compute final value for y
  ADR r4,y ; get address for y
  STR r2,[r4] ; store y

## Slide 19: Example: C assignment
C:
  z = (a << 2) | (b & 15);
Assembler:
ADR r4,a ; get address for a
LDR r0,[r4] ; get value of a
MOV r0,r0,LSL 2 ; perform shift
ADR r4,b ; get address for b
LDR r1,[r4] ; get value of b
AND r1,r1,#15 ; perform AND
ORR r1,r0,r1 ; perform OR

## Slide 20: C assignment, cont’d.
ADR r4,z ; get address for z
STR r1,[r4] ; store value for z

## Slide 21: Additional addressing modes
Base-plus-offset addressing:
  LDR r0,[r1,#16]
  Loads from location r1+16
Auto-indexing increments base register:
  LDR r0,[r1,#16]!
Post-indexing fetches, then does offset:
  LDR r0,[r1],#16
  Loads r0 from r1, then adds 16 to r1.

## Slide 22: ARM flow of control
All operations can be performed conditionally, testing CPSR:
  EQ, NE, CS, CC, MI, PL, VS, VC, HI, LS, GE, LT, GT, LE
Branch operation:
  B #100
  Can be performed conditionally.

## Slide 23: Example: if statement
C:
  if (a > b) { x = 5; y = c + d; } else x = c - d;
Assembler:
; compute and test condition
ADR r4,a ; get address for a
LDR r0,[r4] ; get value of a
ADR r4,b ; get address for b
LDR r1,[r4] ; get value for b
CMP r0,r1 ; compare a < b
BGE fblock ; if a >= b, branch to false block

## Slide 24: If statement, cont’d.
; true block
MOV r0,#5 ; generate value for x
ADR r4,x ; get address for x
STR r0,[r4] ; store x
ADR r4,c ; get address for c
LDR r0,[r4] ; get value of c
ADR r4,d ; get address for d
LDR r1,[r4] ; get value of d
ADD r0,r0,r1 ; compute y
ADR r4,y ; get address for y
STR r0,[r4] ; store y
B after ; branch around false block

## Slide 25: If statement, cont’d.
; false block
fblock ADR r4,c ; get address for c
LDR r0,[r4] ; get value of c
ADR r4,d ; get address for d
LDR r1,[r4] ; get value for d
SUB r0,r0,r1 ; compute a-b
ADR r4,x ; get address for x
STR r0,[r4] ; store value of x
after ...

## Slide 26: Example: switch statement
C:
  switch (test) { case 0: … break; case 1: … }
Assembler:
ADR r2,test ; get address for test
LDR r0,[r2] ; load value for test
ADR r1,switchtab ; load address for switch table
LDR r1,[r1,r0,LSL #2] ; index switch table
switchtab DCD case0
DCD case1
...

## Slide 27: Example: FIR filter
C:
  for (i=0, f=0; i<N; i++)
  f = f + c[i]*x[i];
Assembler
; loop initiation code
MOV r0,#0 ; use r0 for I
MOV r8,#0 ; use separate index for arrays
ADR r2,N ; get address for N
LDR r1,[r2] ; get value of N
MOV r2,#0 ; use r2 for f

## Slide 28: FIR filter, cont’.d
ADR r3,c ; load r3 with base of c
ADR r5,x ; load r5 with base of x
; loop body
loop LDR r4,[r3,r8] ; get c[i]
LDR r6,[r5,r8] ; get x[i]
MUL r4,r4,r6 ; compute c[i]*x[i]
ADD r2,r2,r4 ; add into running sum
ADD r8,r8,#4 ; add one word offset to array index
ADD r0,r0,#1 ; add 1 to i
CMP r0,r1 ; exit?
BLT loop ; if i < N, continue

## Slide 29: ARM subroutine linkage
Branch and link instruction:
  BL foo
  Copies current PC to r14.
To return from subroutine:
  MOV r15,r14

## Slide 30: Nested subroutine calls
Nesting/recursion requires coding convention:
f1 LDR r0,[r13] ; load arg into r0 from stack
; call f2()
STR r13!,[r14] ; store f1’s return adrs
STR r13!,[r0] ; store arg to f2 on stack
BL f2 ; branch and link to f2
; return from f1()
SUB r13,#4 ; pop f2’s arg off stack
LDR r13!,r15 ; restore register and return

## Slide 31: Summary
Load/store architecture
Most instructions are RISCy, operate in single cycle.
  Some multi-register operations take longer.
All instructions can be executed conditionally.