## Slide 1: Introduction
Example: model train controller.

## Slide 2: Purposes of example
Follow a design through several levels of abstraction.
Gain experience with UML.

## Slide 3: Model train setup
console
power
supply
rcvr
motor
ECC
address
header
command

## Slide 4: Requirements
Console can control 8 trains on 1 track.
Throttle has at least 63 levels.
Inertia control adjusts responsiveness with at least 8 levels.
Emergency stop button.
Error detection scheme on messages.

## Slide 5: Requirements form

## Slide 6: Use case
console
train 1
train 2
Select train 1
Set train 1 speed
Select train 1
Set train 1 speed

## Slide 7: Digital Command Control
DCC created by model railroad hobbyists, picked up by industry.
Defines way in which model trains, controllers communicate.
  Leaves many system design aspects open, allowing competition.
This is a simple example of a big trend:
  Cell phones, digital TV rely on standards.

## Slide 8: DCC documents
Standard S-9.1, DCC Electrical Standard.
  Defines how bits are encoded on the rails.
Standard S-9.2, DCC Communication Standard.
  Defines packet format and semantics.

## Slide 9: DCC electrical standard
Voltage moves around the power supply voltage; adds no DC component.
1 is 58 ms, 0 is at least 100 ms.
time
logic 1
logic 0
58 ms
>= 100 ms

## Slide 10: DCC communication standard
Basic packet format: PSA(sD)+E.
P: preamble = 1111111111.
S: packet start bit = 0.
A: address data byte.
s: data byte start bit.
D: data byte (data payload).
E: packet end bit = 1.

## Slide 11: DCC packet types
Baseline packet: minimum packet that must be accepted by all DCC implementations.
  Address data byte gives receiver address.
  Instruction data byte gives basic instruction.
  Error correction data byte gives ECC.

## Slide 12: Conceptual specification
Before we create a detailed specification, we will make an initial, simplified specification.
  Gives us practice in specification and UML.
  Good idea in general to identify potential problems before investing too much effort in detail.

## Slide 13: Basic system commands

## Slide 14: Typical control sequence
:console
:train_rcvr
set-inertia
set-speed
set-speed
set-speed
estop

## Slide 15: Message classes
command
set-inertia
value: unsigned-
integer
set-speed
value: integer
estop

## Slide 16: Roles of message classes
Implemented message classes derived from message class.
  Attributes and operations will be filled in for detailed specification.
Implemented message classes specify message type by their class.
  May have to add type as parameter to data structure in implementation.

## Slide 17: Subsystem collaboration diagram
Shows relationship between console and receiver (ignores role of track):
:console
:receiver
1..n: command

## Slide 18: System structure modeling
Some classes define non-computer components.
  Denote by *name.
Choose important systems at this point to show basic relationships.

## Slide 19: Major subsystem roles
Console:
  read state of front panel;
  format messages;
  transmit messages.
Train:
  receive message;
  interpret message;
  control the train.

## Slide 20: Console system classes
console
panel
formatter
transmitter
receiver*
sender*
1
1
1
1
1
1
1
1
1
1

## Slide 21: Console class roles
panel: describes analog knobs and interface hardware.
formatter: turns knob settings into bit streams.
transmitter: sends data on track.

## Slide 22: Train system classes
train set
train
receiver
controller
motor
interface
detector*
pulser*
1
1..t
1
1
1
1
1
1
1
1
1
1

## Slide 23: Train class roles
receiver: digitizes signal from track.
controller: interprets received commands and makes control decisions.
motor interface: generates signals required by motor.

## Slide 24: Detailed specification
We can now fill in the details of the conceptual specification:
  more classes;
  behaviors.
Sketching out the spec first helps us understand the basic relationships in the system.

## Slide 25: Train speed control
Motor controlled by pulse width modulation:
V
+
-
duty
cycle

## Slide 26: Console physical object classes
knobs*
train-knob: integer
speed-knob: integer
inertia-knob: unsigned-
integer
emergency-stop: boolean
pulser*
pulse-width: unsigned-
integer
direction: boolean
sender*
send-bit()
detector*
read-bit() : integer

## Slide 27: Panel and motor interface classes
panel
train-number() : integer
speed() : integer
inertia() : integer
estop() : boolean
new-settings()
motor-interface
speed: integer

## Slide 28: Class descriptions
panel class defines the controls.
  new-settings() behavior reads the controls.
motor-interface class defines the motor speed held as state.

## Slide 29: Transmitter and receiver classes
transmitter
send-speed(adrs: integer,
speed: integer)
send-inertia(adrs: integer,
val: integer)
set-estop(adrs: integer)
receiver
current: command
new: boolean
read-cmd()
new-cmd() : boolean
rcv-type(msg-type:
command)
rcv-speed(val: integer)
rcv-inertia(val:integer)

## Slide 30: Class descriptions
transmitter class has one behavior for each type of message sent.
receiver function provides methods to:
  detect a new message;
  determine its type;
  read its parameters (estop has no parameters).

## Slide 31: Formatter class
formatter
current-train: integer
current-speed[ntrains]: integer
current-inertia[ntrains]:
unsigned-integer
current-estop[ntrains]: boolean
send-command()
panel-active() : boolean
operate()

## Slide 32: Formatter class description
Formatter class holds state for each train, setting for current train.
The operate() operation performs the basic formatting task.

## Slide 33: Control input cases
Use a soft panel to show current panel settings for each train.
Changing train number:
  must change soft panel settings to reflect current train’s speed, etc.
Controlling throttle/inertia/estop:
  read panel, check for changes, perform command.

## Slide 34: Control input sequence diagram
:knobs
:panel
:formatter
:transmitter
change in speed/
inertia/estop
change in
train number
change in
control
settings
read panel
panel settings
panel-active
send-command
send-speed,
send-inertia.
send-estop
read panel
panel settings
read panel
panel settings
change in
train
number
set-knobs
new-settings

## Slide 35: Formatter operate behavior
idle
update-panel()
send-command()
panel-active()
new train number
other

## Slide 36: Panel-active behavior
panel*:read-train()
current-train = train-knob
update-screen
changed = true
T
panel*:read-speed()
current-speed = throttle
changed = true
T
F
...
F
...

## Slide 37: Controller class
controller
current-train: integer
current-speed: integer
current-direction: boolean
current-inertia: unsigned-integer
operate()
issue-command()

## Slide 38: Setting the speed
Don’t want to change speed instantaneously.
Controller should change speed gradually by sending several commands.

## Slide 39: Sequence diagram for set-speed command
:receiver
:controller
:motor-interface
:pulser*
new-cmd
cmd-type
rcv-speed
set-speed
set-pulse
set-pulse
set-pulse
set-pulse
set-pulse

## Slide 40: Controller operate behavior
issue-command()
receive-command()
wait for a
command
from receiver

## Slide 41: Refined command classes
command
type: 3-bits
address: 3-bits
parity: 1-bit
set-inertia
type=001
value: 3-bits
set-speed
type=010
value: 7-bits
estop
type=000

## Slide 42: Summary
Separate specification and programming.
  Small mistakes are easier to fix in the spec.
  Big mistakes in programming cost a lot of time.
You can’t completely separate specification and architecture.
  Make a few tasteful assumptions.