## Slide 1: Computing Platforms
Example: audio player

## Slide 2: Audio theory of operation
MP3 is widely used audio format, many other formats are in use.
Audio compression uses perceptual coding.
  Some features of audio may not be perceptible.
  Removing unnecessary features can reduce size of the data.

## Slide 3: MPEG audio standards
Layer 1:
  Lossless compression of subbands + optional simple masking model
Layer 2:
  More advanced masking model.
Layer 3:
  Additional processing for lower bit rates.

## Slide 4: MPEG audio rates
Input sampling rates:
  32, 44.1, 48 kHz.
Output bit rates:
  23, 48, 64, 96, 112, 128, 192, 256, 384 kbits/sec.
Output can be mono, dual-channel (bilingual, etc.), stereo.

## Slide 5: Other standards
Dolby Digital (AC-3):
  Uses modified discrete cosine transform.
ATRAC (MiniDisc):
  Uses subband + modified DCT.
MPEG-2 AAC.

## Slide 6: MPEG Layer 1
384 samples/block at all frequencies.
  Equals 8 ms at 48 kHz.
Optional masking model.
  Driven by separate FFT for better accuracy.

## Slide 7: MPEG Layer 1 data frame
Bit allocation codes specify word length in each subband.
Scale factors give gain for each band.
header
CRC
bit
allocation
scale
factors
subband samples
aux
data

## Slide 8: MPEG Layer 1 encoder
Filter
bank
Choose
Scale factor
Masking
model
requantize
*
FFT
mux
0101..

## Slide 9: MPEG Layer 1 encoder operations
Filter bank divides signal into subbands.
Masking model chooses audio features to ignore.
Quantizer chooses number of bits.
Scale factor fits signal within 6 bit range.

## Slide 10: MPEG Layer 1 decoder
0101..
demux
Scale
factor
*
*
Step
size
Inverse
filter
bank
inverse
quantize
expand

## Slide 11: MPEG Layer 1 decoder operations
Decoding is less computationally expensive:
  Apply step size, scaling, inverse quantization.
  Combine subbands.

## Slide 12: Audio player requirements
Category | Description
Name | Audio player.
Purpose | Play audio from file.
Inputs | Flash socket, on/off, play/stop, menu up/down.
Outputs | Speaker
Functions | Display list of files in memory, select file to play, play file.
Performance | Sufficient for audio playback.
Power | 1 AAA battery.
Physical weight/size | Approx. 1” x 2”, less than 2 oz.

## Slide 13: Audio player classes

## Slide 14: File display/state selection

## Slide 15: Audio playback

## Slide 16: Component design and testing
Audio decompression, file system can be acquired as software IP or created from scratch.
If flash is not transferrable, non-standard file system may be useful.
File system and audio decompression can be tested separately.

## Slide 17: Cirrus platform architecture