## Slide 1: Program design and analysis
Software components.
Representations of programs.
Assembly and linking.

## Slide 2: Software state machine
State machine keeps internal state as a variable, changes state based on inputs.
Uses:
  control-dominated code;
  reactive systems.

## Slide 3: State machine example
idle
buzzer
seated
belted
no seat/-
seat/timer on
no belt
and no
timer/-
no belt/timer on
belt/-
belt/
buzzer off
Belt/buzzer on
no seat/-
no seat/
buzzer off

## Slide 4: C implementation
#define IDLE 0
#define SEATED 1
#define BELTED 2
#define BUZZER 3
switch (state) {
case IDLE: if (seat) { state = SEATED; timer_on = TRUE; }
break;
case SEATED: if (belt) state = BELTED;
else if (timer) state = BUZZER;
break;
…
}

## Slide 5: Signal processing and circular buffer
Commonly used in signal processing:
  new data constantly arrives;
  each datum has a limited lifetime.
Use a circular buffer to hold the data stream.
d1
d2
d3
d4
d5
d6
d7
time t
time t+1

## Slide 6: Circular buffer
x1
x2
x3
x4
x5
x6
t1
t2
t3
Data stream
x1
x2
x3
x4
Circular buffer
x5
x6
x7

## Slide 7: Circular buffers
Indexes locate currently used data, current input data:
d1
d2
d3
d4
time t1
use
input
d5
d2
d3
d4
time t1+1
use
input

## Slide 8: Circular buffer in C
#define CMAX 6 /* filter order */
int circ[CMAX]; /* circular buffer */
int pos; /* position of current sample */
void circ_update(int xnew) {
/* compute the new head value with wraparound; the pos pointer moves from 0 to CMAX-1 */
pos = ((pos == CMAX-1) ? 0 : (pos+1));
/* insert the new value at the new head */
circ[pos] = xnew;
}

## Slide 9: Circular buffer in C, cont’d.
void circ_init() {
int i;
for (i=0; i<CMAX; i++) /* set values to 0 */
circ[i] = 0; pos=CMAX-1; /* start at tail so first element will be at 0 */
}
int circ_get(int i) {
int ii;
/* compute the buffer position */
ii = (pos - i) % CMAX;
return circ[ii]; /* return the value */
}

## Slide 10: FIR filter

## Slide 11: FIR filter update function
void circ_update(int xnew) {
/* add the new sample and push off the oldest one */
/* compute the new head value with wraparound; the pos pointer moves from CMAX-1 down to 0 */
pos = ((pos == 0) ? CMAX-1 : (pos-1));
/* insert the new value at the new head */
circ[pos] = xnew;
}

## Slide 12: FIR filter using circular buffer
int fir(int xnew) {
/* given a new sample value, update the queue and compute the filter output */
int i;
int result; /* holds the filter output */
circ_update(xnew); /* put the new value in */
for (i=0, result=0; i<CMAX; i++)
result += b[i] * circ_get(i);
return result;
}

## Slide 13: IIR direct form type II filter

## Slide 14: IIR filter in C
int iir2(int xnew) {
int i, aside, bside, result;
for (i=0, aside=0; i<ZMAX; i++)
aside += -a[i+1] * circ_get(i);
for (i=0, bside=0; i<ZMAX; i++)
bside += b[i+1] * circ_get(i);
result = b[0] * (xnew + aside) + bside;
circ_update(xnew); /* put the new value in */
return result;
}

## Slide 15: Array-based queue in C
#define Q_SIZE 5 /* your queue size may vary */
#define Q_MAX (Q_SIZE-1) /* this is the maximum index value into the array */
int q[Q_SIZE]; /* the array for our queue */
int head, tail; /* indexes for the current queue head and tail */
void queue_init() {
/* initialize the queue data structure */
head = 0;
tail = 0;
}

## Slide 16: Array based queue, cont’d.
void enqueue(int val) {
if (((tail+1) % Q_SIZE) == head) error("enqueue onto full queue",tail);
q[tail] = val;
/* update the tail */
if (tail == Q_MAX)
tail = 0;
else
tail++;
}

## Slide 17: Array based queue, cont’d.
int dequeue() {
int returnval;
if (head == tail) error("dequeue from empty queue",head);
returnval = q[head];
if (head == Q_MAX)
head = 0;
else
head++;
return returnval;
}

## Slide 18: Producer-consumer system
Queues allow varying input and output rates.

## Slide 19: Models of programs
Source code is not a good representation for programs:
  clumsy;
  leaves much information implicit.
Compilers derive intermediate representations to manipulate and optiize the program.

## Slide 20: Data flow graph
DFG: data flow graph.
Does not represent control.
Models basic block: code with no entry or exit.
Describes the minimal ordering requirements on operations.

## Slide 21: Single assignment form
x = a + b;
y = c - d;
z = x * y;
y = b + d;
original basic block
x = a + b;
y = c - d;
z = x * y;
y1 = b + d;
single assignment form

## Slide 22: Data flow graph
x = a + b;
y = c - d;
z = x * y;
y1 = b + d;
single assignment form
+
-
+
*
DFG
a
b
c
d
z
x
y
y1

## Slide 23: DFGs and partial orders
Partial order:
a+b, c-d; b+d x*y
Can do pairs of operations in any order.
+
-
+
*
a
b
c
d
z
x
y
y1

## Slide 24: Control-data flow graph
CDFG: represents control and data.
Uses data flow graphs as components.
Two types of nodes:
  decision;
  data flow.

## Slide 25: Data flow node
Encapsulates a data flow graph:
Write operations in basic block form for simplicity.
x = a + b;
y = c + d

## Slide 26: Control
cond
T
F
Equivalent forms
value
v1
v2
v3
v4

## Slide 27: CDFG example
if (cond1) bb1();
else bb2();
bb3();
switch (test1) {
case c1: bb4(); break;
case c2: bb5(); break;
case c3: bb6(); break;
}
cond1
bb1()
bb2()
bb3()
bb4()
test1
bb5()
bb6()
T
F
c1
c2
c3

## Slide 28: for loop
for (i=0; i<N; i++)
loop_body();
for loop
i=0;
while (i<N) {
loop_body(); i++; }
equivalent
i<N
loop_body()
T
F
i=0

## Slide 29: Assembly and linking
Last steps in compilation:
HLL
compile
assembly
assemble
HLL
HLL
assembly
assembly
link
executable
load
assembly
assembly
object

## Slide 30: Multiple-module programs
Programs may be composed from several files.
Addresses become more specific during processing:
  relative addresses are measured relative to the start of a module;
  absolute addresses are measured relative to the start of the CPU address space.

## Slide 31: Assemblers
Major tasks:
  generate binary for symbolic instructions;
  translate labels into addresses;
  handle pseudo-ops (data, etc.).
Generally one-to-one translation.
Assembly labels:
  ORG 100
  label1 ADR r4,c

## Slide 32: Symbol table
ADD r0,r1,r2
xx ADD r3,r4,r5
CMP r0,r3
yy SUB r5,r6,r7
assembly code
xx 0x8
yy 0x10
symbol table

## Slide 33: Symbol table generation
Use program location counter (PLC) to determine address of each location.
Scan program, keeping count of PLC.
Addresses are generated at assembly time, not execution time.

## Slide 34: Symbol table example
ADD r0,r1,r2
xx ADD r3,r4,r5
CMP r0,r3
yy SUB r5,r6,r7
xx 0x8
yy 0x10
PLC=0x7
PLC=0x8
PLC=0x9
PLC=0x10

## Slide 35: Two-pass assembly
Pass 1:
  generate symbol table
Pass 2:
  generate binary instructions

## Slide 36: Relative address generation
Some label values may not be known at assembly time.
Labels within the module may be kept in relative form.
Must keep track of external labels---can’t generate full binary for instructions that use external labels.

## Slide 37: Pseudo-operations
Pseudo-ops do not generate instructions:
  ORG sets program location.
  EQU generates symbol table entry without advancing PLC.
  Data statements define data blocks.

## Slide 38: Linking
Combines several object modules into a single executable module.
Jobs:
  put modules in order;
  resolve labels across modules.

## Slide 39: Externals and entry points
external reference
entry point
xxx ADD r1,r2,r3
B a
yyy %1
a ADR r4,yyy
ADD r3,r4,r5

## Slide 40: Module ordering
Code modules must be placed in absolute positions in the memory space.
Load map or linker flags control the order of modules.
module1
module2
module3

## Slide 41: Dynamic linking
Some operating systems link modules dynamically at run time:
  shares one copy of library among all executing programs;
  allows programs to be updated with new versions of libraries.

## Slide 42: Reentrancy
Interrupting program with another call to the function does not change results.
  Changing global variables compromises reentrancy.
Recursive code:
int foo = 1;
int task1() {
foo = foo + 1;
return foo;
}