## Slide 1: Program design and analysis
Program-level performance analysis.
Optimizing for:
  Execution time.
  Energy/power.
  Program size.
Program validation and testing.

## Slide 2: Program-level performance analysis
Need to understand performance in detail:
  Real-time behavior, not just typical.
  On complex platforms.
Program performance ¹ CPU performance:
  Pipeline, cache are windows into program.
  We must analyze the entire program.

## Slide 3: Complexities of program performance
Varies with input data:
  Different-length paths.
Cache effects.
Instruction-level performance variations:
  Pipeline interlocks.
  Fetch times.

## Slide 4: How to measure program performance
Simulate execution of the CPU.
  Makes CPU state visible.
Measure on real CPU using timer.
  Requires modifying the program to control the timer.
Measure on real CPU using logic analyzer.
  Requires events visible on the pins.

## Slide 5: Program performance metrics
Average-case execution time.
  Typically used in application programming.
Worst-case execution time.
  A component in deadline satisfaction.
Best-case execution time.
  Task-level interactions can cause best-case program behavior to result in worst-case system behavior.

## Slide 6: Elements of program performance
Basic program execution time formula:
  execution time = program path + instruction timing
Solving these problems independently helps simplify analysis.
  Easier to separate on simpler CPUs.
Accurate performance analysis requires:
  Assembly/binary code.
  Execution platform.

## Slide 7: Data-dependent paths in an if statement
if (a || b) { /* T1 */
if ( c ) /* T2 */
x = r*s+t; /* A1 */
else y=r+s; /* A2 */
z = r+s+u; /* A3 */
}
else {
if ( c ) /* T3 */
y = r-t; /* A4 */
}
a | b | c | path
0 | 0 | 0 | T1=F, T3=F: no assignments
0 | 0 | 1 | T1=F, T3=T: A4
0 | 1 | 0 | T1=T, T2=F: A2, A3
0 | 1 | 1 | T1=T, T2=T: A1, A3
1 | 0 | 0 | T1=T, T2=F: A2, A3
1 | 0 | 1 | T1=T, T2=T: A1, A3
1 | 1 | 0 | T1=T, T2=F: A2, A3
1 | 1 | 1 | T1=T, T2=T: A1, A3

## Slide 8: Paths in a loop
for (i=0, f=0; i<N; i++)
f = f + c[i] * x[i];
i=0
f=0
i=N
f = f + c[i] * x[i]
i = i + 1
N
Y

## Slide 9: Paths in a loop with conditions
for (i=0, f=0; i<N; i++) {
if (x[i] > 0)
f = f + c[i] * x[i];
}
i=0;
f=0;
i<N
x[i] > 0
f =f + c[i] * x[i];
i++;
T
F
T
F
executed 1 time
executed N+1 times
executed N times
executed N times
executed times

## Slide 10: Instruction timing
Not all instructions take the same amount of time.
  Multi-cycle instructions.
  Fetches.
Execution times of instructions are not independent.
  Pipeline interlocks.
  Cache effects.
Execution times may vary with operand value.
  Floating-point operations.
  Some multi-cycle integer operations.

## Slide 11: Caching effects
for (i = 0, f = 0; i < N; i++)
f = f + c[i] * x[i];
Word 0
Word 1
Word 2
Word 3
line 0
Word 4
Word 5
Word 6
Word 7
line 1
First access to a cache line causes a miss and prefetch.
Later accesses to that line result in cache hits.

## Slide 12: Mesaurement-driven performance analysis
Not so easy as it sounds:
  Must actually have access to the CPU.
  Must know data inputs that give worst/best case performance.
  Must make state visible.
Still an important method for performance analysis.

## Slide 13: Feeding the program
Need to know the desired input values.
May need to write software scaffolding to generate the input values.
Software scaffolding may also need to examine outputs to generate feedback-driven inputs.

## Slide 14: Trace-driven measurement
Trace-driven:
  Instrument the program.
  Save information about the path.
Requires modifying the program.
Trace files are large.
Widely used for cache analysis.

## Slide 15: Physical measurement
In-circuit emulator allows tracing.
  Affects execution timing.
Logic analyzer can measure behavior at pins.
  Address bus can be analyzed to look for events.
  Code can be modified to make events visible.
Particularly important for real-world input streams.

## Slide 16: CPU simulation
Some simulators are less accurate.
Cycle-accurate simulator provides accurate clock-cycle timing.
  Simulator models CPU internals.
  Simulator writer must know how CPU works.

## Slide 17: SimpleScalar FIR filter simulation
int x[N] = {8, 17, … };
int c[N] = {1, 2, … };
main() {
int i, k, f;
for (k=0; k<COUNT; k++)
for (i=0; i<N; i++)
f += c[i]*x[i];
}
COUNT | total sim cycles | sim cycles per filter execution
100 | 25854 | 259
1,000 | 155759 | 156
1,0000 | 1451840 | 145

## Slide 18: Performance optimization motivation
Embedded systems must often meet deadlines.
  Faster may not be fast enough.
Need to be able to analyze execution time.
  Worst-case, not typical.
Need techniques for reliably improving execution time.

## Slide 19: Programs and performance analysis
Best results come from analyzing optimized instructions, not high-level language code:
  non-obvious translations of HLL statements into instructions;
  code may move;
  cache effects are hard to predict.

## Slide 20: Loop optimizations
Loops are good targets for optimization.
Basic loop optimizations:
  code motion;
  induction-variable elimination;
  strength reduction (x*2 -> x<<1).

## Slide 21: Code motion
for (i=0; i<N*M; i++)
z[i] = a[i] + b[i];
i<N*M
i=0;
z[i] = a[i] + b[i];
i = i+1;
N
Y
i<X
i=0; X = N*M

## Slide 22: Induction variable elimination
Induction variable: loop index.
Consider loop:
  for (i=0; i<N; i++)
  for (j=0; j<M; j++)
  z[i,j] = b[i,j];
Rather than recompute i*M+j for each array in each iteration, share induction variable between arrays, increment at end of loop body.

## Slide 23: Cache analysis
Loop nest: set of loops, one inside other.
Perfect loop nest: no conditionals in nest.
Because loops use large quantities of data, cache conflicts are common.

## Slide 24: Array conflicts in cache
a[0,0]
b[0,0]
main memory
cache
1024
4099
...
1024
4099

## Slide 25: Array conflicts, cont’d.
Array elements conflict because they are in the same line, even if not mapped to same location.
Solutions:
  move one array;
  pad array to change alignment.

## Slide 26: Array padding
Add array elements to change mapping into cache:
a[0,0]
a[0,1]
a[0,2]
a[1,0]
a[1,1]
a[1,2]
before
a[0,0]
a[0,1]
a[0,2]
a[1,0]
a[1,1]
a[1,2]
after
a[0,2]
a[1,2]

## Slide 27: Loop tiling
Breaks one loop into a nest of loops.
Changes order of accesses within array.
  Changes cache behavior.

## Slide 28: Loop tiling example
for (i=0; i<N; i++) {
for (j=0; j<N; j++) {
z[i][j] = x[i] * y[j];
}
}
for (j=0; j < N; j += TILE) {
for (i=0; i<N; i++) {
for (jj=0; j<TILE; jj++) {
z[i][j + jj] = x[i] * y[j + jj];
}
}
}
x[]
y[]
x[0]
y[0]
y[1]
y[N-1]
x[]
y[]
y[0]
y[1]
x[0]
x[1]
y[0]
y[1]

## Slide 29: Performance optimization hints
Use registers efficiently.
Use page mode memory accesses.
Analyze cache behavior:
  instruction conflicts can be handled by rewriting code, rescheudling;
  conflicting scalar data can easily be moved;
  conflicting array data can be moved, padded.

## Slide 30: Energy/power optimization
Energy: ability to do work.
  Most important in battery-powered systems.
Power: energy per unit time.
  Important even in wall-plug systems---power becomes heat.

## Slide 31: Measuring energy consumption
Execute a small loop, measure current:
while (TRUE)
a();
I

## Slide 32: Sources of energy consumption
Relative energy per operation (Catthoor et al):
  memory transfer: 33
  external I/O: 10
  SRAM write: 9
  SRAM read: 4.4
  multiply: 3.6
  add: 1

## Slide 33: Cache behavior is important
Energy consumption has a sweet spot as cache size changes:
  cache too small: program thrashes, burning energy on external memory accesses;
  cache too large: cache itself burns too much power.

## Slide 34: Cache sweet spot
[Li98] © 1998 IEEE

## Slide 35: Optimizing for energy
First-order optimization:
  high performance = low energy.
Not many instructions trade speed for energy.

## Slide 36: Optimizing for energy, cont’d.
Use registers efficiently.
Identify and eliminate cache conflicts.
Moderate loop unrolling eliminates some loop overhead instructions.
Eliminate pipeline stalls.
Inlining procedures may help: reduces linkage, but may increase cache thrashing.

## Slide 37: Efficient loops
General rules:
  Don’t use function calls.
  Keep loop body small to enable local repeat (only forward branches).
  Use unsigned integer for loop counter.
  Use <= to test loop counter.
  Make use of compiler---global optimization, software pipelining.

## Slide 38: Single-instruction repeat loop example
STM #4000h,AR2
; load pointer to source
STM #100h,AR3
; load pointer to destination
RPT #(1024-1)
MVDD *AR2+,*AR3+
; move

## Slide 39: Optimizing for program size
Goal:
  reduce hardware cost of memory;
  reduce power consumption of memory units.
Two opportunities:
  data;
  instructions.

## Slide 40: Data size minimization
Reuse constants, variables, data buffers in different parts of code.
  Requires careful verification of correctness.
Generate data using instructions.

## Slide 41: Reducing code size
Avoid function inlining.
Choose CPU with compact instructions.
Use specialized instructions where possible.

## Slide 42: Program validation and testing
But does it work?
Concentrate here on functional verification.
Major testing strategies:
  Black box doesn’t look at the source code.
  Clear box (white box) does look at the source code.

## Slide 43: Clear-box testing
Examine the source code to determine whether it works:
  Can you actually exercise a path?
  Do you get the value you expect along a path?
Testing procedure:
  Controllability: rovide program with inputs.
  Execute.
  Observability: examine outputs.

## Slide 44: Controlling and observing programs
firout = 0.0;
for (j=curr, k=0; j<N; j++, k++)
firout += buff[j] * c[k];
for (j=0; j<curr; j++, k++)
firout += buff[j] * c[k];
if (firout > 100.0) firout = 100.0;
if (firout < -100.0) firout = -100.0;
Controllability:
  Must fill circular buffer with desired N values.
  Other code governs how we access the buffer.
Observability:
  Want to examine firout before limit testing.

## Slide 45: Execution paths and testing
Paths are important in functional testing as well as performance analysis.
In general, an exponential number of paths through the program.
  Show that some paths dominate others.
  Heuristically limit paths.

## Slide 46: Choosing the paths to test
Possible criteria:
  Execute every statement at least once.
  Execute every branch direction at least once.
Equivalent for structured programs.
Not true for gotos.
not covered

## Slide 47: Basis paths
Approximate CDFG with undirected graph.
Undirected graphs have basis paths:
  All paths are linear combinations of basis paths.

## Slide 48: Cyclomatic complexity
Cyclomatic complexity is a bound on the size of basis sets:
  e = # edges
  n = # nodes
  p = number of graph components
  M = e – n + 2p.

## Slide 49: Branch testing
Heuristic for testing branches.
  Exercise true and false branches of conditional.
  Exercise every simple condition at least once.

## Slide 50: Branch testing example
Correct:
  if (a || (b >= c)) { printf(“OK\n”); }
Incorrect:
  if (a && (b >= c)) { printf(“OK\n”); }
Test:
  a = F
  (b >=c) = T
Example:
  Correct: [0 || (3 >= 2)] = T
  Incorrect: [0 && (3 >= 2)] = F

## Slide 51: Domain testing
Heuristic test for linear inequalities.
Test on each side + boundary of inequality.

## Slide 52: Def-use pairs
Variable def-use:
  Def when value is assigned (defined).
  Use when used on right-hand side.
Exercise each def-use pair.
  Requires testing correct path.

## Slide 53: Loop testing
Loops need specialized tests to be tested efficiently.
Heuristic testing strategy:
  Skip loop entirely.
  One loop iteration.
  Two loop iterations.
  # iterations much below max.
  n-1, n, n+1 iterations where n is max.

## Slide 54: Black-box testing
Complements clear-box testing.
  May require a large number of tests.
Tests software in different ways.

## Slide 55: Black-box test vectors
Random tests.
  May weight distribution based on software specification.
Regression tests.
  Tests of previous versions, bugs, etc.
  May be clear-box tests of previous versions.

## Slide 56: How much testing is enough?
Exhaustive testing is impractical.
One important measure of test quality---bugs escaping into field.
Good organizations can test software to give very low field bug report rates.
Error injection measures test quality:
  Add known bugs.
  Run your tests.
  Determine % injected bugs that are caught.