## Slide 1: Processes and operating systems
Interprocess communication.
Evaluating RTOS performance.
Example---POSIX.

## Slide 2: Interprocess communication
Interprocess communication (IPC): OS provides mechanisms so that processes can pass data.
Two types of semantics:
  blocking: sending process waits for response;
  non-blocking: sending process continues.

## Slide 3: IPC styles
Shared memory:
  processes have some memory in common;
  must cooperate to avoid destroying/missing messages.
Message passing:
  processes send messages along a communication channel---no common address space.

## Slide 4: Shared memory
Shared memory on a bus:
CPU 1
CPU 2
memory

## Slide 5: Message passing
Message passing on a network:
CPU 1
CPU 2
message
message
message

## Slide 6: freeRTOS.org queues
Queues can be used to pass messages.
Operating system manages queues.
xQueueHandle q1;
q1 = xQueueCreate( MAX_SIZE, sizeof(msg_record));
if (q1 == 0) /* error */
xQueueSend(q1,(void *)msg,(portTickType)0); /* queue, message to send, final parameter controls timeout */
if (xQueueReceive(q2,&(in_msg),0); /* queue, message received, timeout */

## Slide 7: Signals
Similar to a software interrupt.
Changes flow of control but does not pass parameters.
  May be typed to allow several types of signals.
  Unix ^c sends kill signal to process.

## Slide 8: Signals in UML
More general than Unix signal---may carry arbitrary data:
<<signal>>
aSig
p : integer
someClass
sigbehavior()
<<send>>

## Slide 9: Mailbox
Fixed memory or register used for interprocess communication.
May be implemented directly in hardware or by RTOS.
void post(message *msg) {
P(mailbox.sem);
copy(mailbox.data,msg);
mailbox.flag = TRUE
V(mailbox.sem);
}
boolean pickup(message *msg) {
boolean pickup = FALSE;
P(mailbox.sem);
pickup = mailbox.flag;
mailbox.flag = FALSE;
copy(msg, mailbox.data);
V(mailbox.sem);
return(pickup);
}

## Slide 10: RTOS performance
Assumptions:
  Context switch takes zero time.
  Interrupts do not interfere with scheduling.
  Process execution time is known and fixed.
  Process interaction times do not interact.

## Slide 11: Evaluating operating system performance
Context-switching time.
Interrupt latency and critical sections.
Interrupt priorities and interrupt latency.
RTOS performance evaluation.
Caches and performance

## Slide 12: Context-switching time
Non-zero context switch time can push limits of a tight schedule.
Hard to calculate effects---depends on order of context switches.
In practice, OS context switch overhead is small (hundreds of clock cycles) relative to many common task periods (ms – ms).

## Slide 13: Scheduling and context switch overhead
Process | Execution time | deadline
P1 | 3 | 5
P2 | 3 | 10
With context switch overhead of
1, no feasible schedule.
2TP1 + TP2 = 2*(1+3)+(1_3)=11

## Slide 14: Interrupt latency
Interrupts override process priorities.
Interupt handling latency has non-zero hardware latency.
Interrupt service routine (ISR) takes time to execute.

## Slide 15: Interrupt latency in critical sections
Interrupts are turned off in critical section.
Long critical sections add software delays to interrupt latency.
General-purpose operating systems may have long critical sections.

## Slide 16: Interrupt handling architecture
Use two levels of service:
  Interrupt service handler (ISH) is called at interrupt, provides minimal functions.
  Interrupt service routine (ISR) is process invoked by ISH, performs most of the device handling.

## Slide 17: RTOS simulation
Some RTOSs provide scheduling simulators.
Schedule a mix of processes using I/O traces.

## Slide 18: Process execution time
Process execution time is not constant.
Extra CPU time can be good.
Extra CPU time can also be bad:
  Next process runs earlier, causing new preemption.

## Slide 19: Processes and caches
Processes can cause additional caching problems.
  Even if individual processes are well-behaved, processes may interfere with each other.
Worst-case execution time with bad behavior is usually much worse than execution time with good cache behavior.

## Slide 20: Effects of scheduling on the cache
Process | WCET | Avg. CPU time
P1 | 3 | 2
P2 | 2 | 1
P1
P2
0
5
10

## Slide 21: Unix
Unix developed in 1960’s at Bell Laboratories to support text processing.
POSIX is a standard version of Unix.
Linux is an open-source POSIX-compliant operating system.
  Linux versions have been developed to improve real-time responsiveness.

## Slide 22: POSIX process creation
fork() makes two copies of executing process.
Child process identifies itself and overlays new code.
if (childid == 0) {
/* must be child */
execv(“mychild”,childargs);
perror(“execv”);
exit(1);
}
else { /* is the parent */
parent_stuff();
wait(&cstatus);
exit(0);
}

## Slide 23: POSIX real-time scheduling
Processes may run under different scheduling policies.
_POSIX_PRIORITY_SCHEDULING resource supports real-time scheduling.
SCHED_FIFO supports RMS.
int i, my_process_id;
struct sched_param my_sched_params;
...
i = sched_setscheduler(my_process_id,SCHED_FIFO,&sched_params);

## Slide 24: POSIX interprocess communication
Supports counting semaphores in _POSIX_SEMAPHORES.
Supports shared memory.
i = sem_wait(my_semaphore); /* P */
/* do useful work */
i = sem_post(my_semaphore); /* V */
/* sem_trywait tests without blocking */
i = sem_trywait(my_semaphore);

## Slide 25: POSIX pipes
Pipes directly connect programs.
pipe() function creates a pipe to talk to a child before the child is created.
if (pipe(pipe_ends) < 0) {
perror(“pipe”);
break;
}
childid = fork();
if (childid == 0) {
childargs[0] = pipe_ends[1];
execv(“mychild”,childargs);
perror(“execv”);
exit(1);
}
else { ... }

## Slide 26: POSIX message queues
Supports message queues under _POSIX_MESSAGE_PASSING
mq_open() creates named queue.
myq = mq_open(“/q1”,O_CREAT | RDWR,S_IRWXU,&mq_attr);
…
if (mq_send(myq,data,len,priority) < 0) { /* error */ }
nbytes = mq_receive(myq,rcvbuf,MAXLEN,&prio);