## Slide 1: System design techniques
Dependability, safety, security.
  Examples.
Quality assurance.
Verifying the specification.
Design reviews.
Safety-oriented methodologies.

## Slide 2: Dependability, safety, and security
Dependability: length of time for which a system can operate without defects.
Safety and security can be quantified using dependability concepts.

## Slide 3: Therac-25 Medical Imager (Leveson and Turner)
Six known accidents: radiation overdoses leading to death and serious injury.
Radiation gun controlled by PDP-11.
Four major software components:
  stored data;
  scheduler;
  set of tasks;
  interrupt services.

## Slide 4: Therac-25 tasks
Treatment monitor controlled and monitored setup and delivery of treatment in eight phases.
Servo task controlled radiation gun.
Housekeeper task took care of status interlocks and limit checks.

## Slide 5: Therac-25 treatment monitor task
Treat was main monitor task.
  Eight subroutines.
  Treat rescheduled itself after every subroutine.

## Slide 6: Therac-25 software timing race
Timing-dependent use of mode and energy:
  if keyboard handler sets completion behavior before operator changes mode/energy data, Datent task will not detect the change, but Hand task will.

## Slide 7: Therac-25 software timing errors
Changes to parameters made by operator may show on screen but not be sensed by Datent task.
One accident caused by entering mode/energy, changing mode/energy, returning to command line in 8 seconds.
Skilled operators typed faster, more likely to exercise bug.

## Slide 8: Leveson and Turner observations on Therac-25
Performed limited safety analysis: guessed at error probabilities, etc.
Did not use mechanical backups to check machine operation.
Used overly complex programs written in unreliable styles.

## Slide 9: Stuxnet
Series of attacks on Iranian nuclear processing facilities.
Facilities were not directly connected to Internet---air gap.
  Attack code was carried by maintenance workers using USB devices infected on outside machines.

## Slide 10: Quality assurance
Quality judged by how well product satisfies its intended function.
  May be measured in different ways for different kinds of products.
Quality assurance (QA) makes sure that all stages of the design process help to deliver a quality product.

## Slide 11: ISO 9000
Developed by International Standards organization.
Applies to a broad range industries.
Concentrates on process.
Validation based on extensive documentation of organization’s process.

## Slide 12: CMU Capability Maturity Model
Five levels of organizational maturity:
  Initial: poorly organized process, depends on individuals.
  Repeatable: basic tracking mechanisms.
  Defined: processes documented and standardized.
  Managed: makes detailed measurements.
  Optimizing: measurements used for improvement.

## Slide 13: Verification
requirements
bug
Verification and testing are important throughout the design flow.
Early bugs are more expensive to fix:
time
cost to fix
coding bug

## Slide 14: Verifying requirements and specification
Requirements:
  prototypes;
  prototyping languages;
  pre-existing systems.
Specifications:
  usage scenarios;
  formal techniques.

## Slide 15: Design review
Uses meetings to catch design flaws.
  Simple, low-cost.
  Proven by experiments to be effective.
Use other people in the project/company to help spot design problems.

## Slide 16: Design review players
Designers: present design to rest of team, make changes.
Review leader: coordinates process.
Review scribe: takes notes of meetings.
Review audience: looks for bugs.

## Slide 17: Before the design review
Design team prepares documents used to describe the design.
Leader recruits audience, coordinates meetings, distributes handouts, etc.
Audience members familiarize themselves with the documents before they go to the meeting.

## Slide 18: Design review meeting
Leader keeps meeting moving; scribe takes notes.
Designers present the design:
  use handouts;
  explain what is going on;
  go through details.

## Slide 19: Design review audience
Look for any problems:
  Is the design consistent with the specification?
  Is the interface correct?
  How well is the component’s internal architecture designed?
  Did they use good design/coding practices?
  Is the testing strategy adequate?

## Slide 20: Follow-up
Designers make suggested changes.
  Document changes.
Leader checks on results of changes, may distribute to audience for further review or additional reviews.

## Slide 21: Safety-oriented methodologies
Availability: probability of a system’s correct operation over time.
  Often modeled as an exponential distribution.
  , failures per unit time .
Safety analysis phases:
  Hazard analysis: types of safety-related problems that may occur.
  Risk assessment: effects of hazards, severity or likelihood of injury, etc.
  Risk mitigation: design modifications to improve system’s ability to handle identified hazards.

## Slide 22: Safety-oriented standards
ISO 26262: Functional safety management for automotive electrics and electronics (EE).
DO-178C: safety-related procedures for avionics software.
  Failure software level: A catastrophic, B hazardous, C major, D minor, E no effect.
Several SAE standards for automotive software.
MISRA coding standards for C and C++.
CERT C standard for C coding.

## Slide 23: Security and safety-critical systems
Security problems threaten safety.
The air gap myth---today’s systems are vulnerable to software attacks from many sources.
Attack surface: set of program locations and use cases in which system can be attacked.